GEOLOGY 460 – HYDROGEOLOGY

Laboratory 1

Calculating Discharge Using Direct and Indirect Measurements

Introduction

Surface-water records of our nation's streams have become invaluable to hydrologists, geomorphologists, and engineers during the past several decades.  Rapid urbanization has put increasing pressure on the development of areas once considered unsuitable for development, including river floodplains and terraces.  Scientists are increasingly requested to conduct flood hazard studies and project the future behavior of streams.

The USGS has kept annual records of stream discharges and stages of lakes and reservoirs for most of this century, and this information has been useful in projecting the behavior of streams during flood stage.  This data are collected primarily by gaging stations, which record the hourly water level, known as gage height, of a stream.  Unfortunately, gaging stations are few relative to the number of second and third order streams in the United States.  Therefore, other methods to measure discharge are necessary in scientific studies.

This laboratory examines methods of calculating discharge using both direct and indirect measurements.  In most instances, one can directly measure flow velocities by wading in the stream and using a current meter.  This procedure is extremely hazardous during large flooding events; therefore, indirect techniques of measuring discharge are necessary.  Both of these methods are discussed below.

Field Procedures

I. Direct Measurement of Baseflow Discharge:

A. Make a sketch of your cross section in your field book or data sheet. Be sure to indicate the aspect from which your diagram is taken (flow direction, etc.). The terms ‘right bank and left bank’ are in reference to your orientation when facing downstream.

B.  Divide the cross sectional area of the stream into segments.  You will need to first measure the channel width of the stream by stretching a tape from water's edge to water's edge.  Next, divide the cross section into 8-10 segments, and make a depth measurement at the midpoint of each section.

* Record the depth and width of each section in your field book or in the table provided.

C.  Determine the velocity of the stream via the pygmy current meter.  Measure velocity at the midpoint of each section by placing the current meter at the 40% mark in the water column (0%= channel bottom, 100% water surface).  The velocity is calculated by counting the number of clicks per minute, and dividing by 60. This yields values in ft/s. If time allows, conduct three trials, and use the average for the representative velocity for each section.  Record this data in your field book.

D. Determine the velocity of the stream via the Marsh-McBirney meter.  For the same channel

cross section, repeat the same procedure of measuring velocity of the stream, except use the Marsh-McBirney current meter.

E. Determine the velocity of the stream by the “float method”.  Toss into the water a piece of wood or a small furry mammal, and measure its travel distance per time. Do this three times, and take the average. Multiply your average velocity value by 0.8, and record your findings.

F. Measure grain size of the channel bottom as directed by your Instructor.

G. Estimate the Mannings Roughness Coefficient using the tables provided.

H. Estimate bankfull depth

I. Estimate bankfull width

J. Determine slope as indicated by your instructor

Make observations concerning the size and distribution of the sediment supply in the stream channel.  Use this data to estimate Mannings roughness value.

DATA TABLES

Upper Reach or Lower Reach (circle one)

Total Width of Stream:_______

Pygmy meter  (be sure to record your units!)

| Section # | Section Width | Section Depth | Current Meter Reading | Discharge |
| --- | --- | --- | --- | --- |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |
| 6 |  |  |  |  |
| 7 |  |  |  |  |
| 8 |  |  |  |  |
| 9 |  |  |  |  |
| 10 |  |  |  |  |
| 11 |  |  |  |  |

Marsh-McBirney meter (be sure to record your units!)

| Section # | Channel Width | Channel Depth | Current Meter Reading | Discharge |
| --- | --- | --- | --- | --- |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |
| 6 |  |  |  |  |
| 7 |  |  |  |  |
| 8 |  |  |  |  |
| 9 |  |  |  |  |
| 10 |  |  |  |  |
| 11 |  |  |  |  |

Estimation of velocity using “float method”_______

Channel Slope: ______

Particle Size Analysis

| Size (mm) | Count |
| --- | --- |
| <2 |  |
| 2.8 |  |
| 4 |  |
| 5.6 |  |
| 8 |  |
| 11 |  |
| 16 |  |
| 22.6 |  |
| 32 |  |
| 45 |  |
| 64 |  |
| 90 |  |
| 128 |  |
| 180 |  |
| >180 |  |

MEASURE THE INTERMEDIATE AXIS OF THE FIVE LARGEST BOULDERS, AND RECORD THEIR VALUES BELOW:

_______,  _______,  _______,  _______,  _______,

“THE PRODUCT”

Measurements of Discharge

Port Republic, Virginia

(Each answer below should be accompanied with documentation of your work, organized and numbered neatly on a separate page (hand written acceptable). With the exception of shear stress, report your units in values of meters, seconds.

1. Sketch of your cross section, with aspect facing downstream, showing individual cells within your cross section that include values of width, depth, and velocity.

We will assume that mass in = mass out, and that the discharge values for the two cross sections are the same due to the short distance between them. Therefore…..

2.  Calculate the discharge using direct measurements of Marsh-McBirney meter for both the upstream and downstream sections (report in cubic meters per second).  Report the percent difference between these two values.

Where:

percent difference =  {(downstream discharge – upstream discharge)} * 100

(downstream discharge)

3. Calculate discharge using direct measurements of Pygmy Gurley meter for both the upstream and downstream sections (report in cubic meters per second).  Report the percent difference between these two values.

4.  Compare the values of velocity for the pygmy meter versus the Marsh-McBirney meter by using the percent differences.  Which meter is associated with the lowest value of difference?  As a whole, are the values similar or different?  What factors may account for the variability of the data?

5. Measure the surface velocity using the “float” method, and multiply the average by 0.8 (which serves as an estimate of average velocity for the water column).  How does this value compare to the average velocity obtained by the flow meters?  (you can do this quickly by using excel and averaging your current meter velocity for each section).

6. Estimate the Manning Roughness coefficient, using field observations and tables provided.

7. Calculate Mannings roughness coefficient by using the Manning Equation, your average discharge of your four values of Q, and your field measurements of slope and mean channel width and depth (hydraulic radius and area).

8. Compare your estimated and calculated values of roughness for the reach, and report the percent difference.  If the values are significantly different (say, more than 25%), give a plausible explanation of why this is the case.

9.  Using the equations from our lectures and your average value of the intermediate axis of the 5 largest boulders from your field data, determine the maximum velocity and maximum depth required to mobilize this load.

10. Determine the median grain sizes (D50) for upstream and downstream reaches.

11.  Using the equation below (found in your Powerpoint lecture), determine the critical flow depth to mobilize the D50 particle for the upstream and downstream cross sections of the stream.

hc =(ρs – ρw) τ*c  D50

ρwS

12. Compare your critical flow depth value (question 11) to your estimated ‘bankfull flow’ (2.00 meters) determined with your clinometer and stadia rod.

What is the percent difference between these values?  Does bankfull depth seem to coincide with your critical flow depth?

13. Using the shear stress equation (τc = hc ρw g S), determine the critical boundary shear stress for the upstream and downstream cross sections of the stream (report in units of g/cm-s2.)

# 14.  Consider the flow conditions observed on Friday in the stream, including the water level and its clarity. Based on your observations, do you think overland flow was a major component of the total flow observed on Friday? Why or why not?  If no, of the different components that make up the total flow of the hydrograph (overland, baseflow, interflow), what do you think is the origin of the water we saw on Friday?