Ground Water Flow to Wells

Due: Monday, Dec. 3 @ 4 p.m.

1.  Plot the values of 1/u versus W(u) given in the table in Appendix 1 of Fetter (also given to you in a class handout) on log-log paper using Excel (note that the table gives you values of u and not 1/u).  It is only necessary to plot the values lying in the range 0.1 < 1/u < 10,000.  The curve that you have plotted is the Theis Curve. Because we are very short on time, I have saved you the headache, and have provided you the Theis curve (link is on the website). Therefore, please skip this question.

2.  The thickness of a horizontal, confined, homogeneous, isotropic aquifer of infinite aerial extent is 30 m.  A well fully penetrating the aquifer was continuously pumped at a constant rate of 0.1 m3/sec for a period of 1 day.  The drawdowns given below were observed in a fully penetrating observation well 90 m from the pumping well.  Compute the transmissivity and storativity by using:

a)  The Theis method of log-log matching (using the type curve prepared in problem 1)

- The Jacob method of semi log plotting

- Record your answers in units of meters, seconds.

Be sure that the log scaling of your Theis graph and drawdown graphs are the same.

| time (min) | h0-h (m) | time (min) | h0-h (m) | time (min) | h0-h (m) | time (min) | h0-h (m) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.14 | 7 | 0.39 | 40 | 0.66 | 100 | 0.81 |
| 2 | 0.22 | 8 | 0.40 | 50 | 0.70 | 200 | 0.90 |
| 3 | 0.28 | 9 | 0.42 | 60 | 0.71 | 400 | 0.99 |
| 4 | 0.32 | 10 | 0.44 | 70 | 0.73 | 800 | 1.07 |
| 5 | 0.34 | 21 | 0.55 | 80 | 0.76 | 1000 | 1.10 |
| 6 | 0.37 | 30 | 0.62 | 90 | 0.79 |  |  |

3.  You are asked to design a pump test for a confined aquifer in which the transmissivity is expected to be about 1.4 * 10- 2   m2/s and the storativity about 1.0 * 10- 4.  What pumping rate would you recommend for the test if it is desired that there be an easily measured drawdown of at least 1 m during the first 6 hours of the test in an observation well 150 m from the pumping well?

4.  A well is continuously pumped at 144,375 ft3/day for 30 days.  Eight proximal wells show the resulting drawdowns from the pumping.  Calculate the transmissivity (ft2/day) and storativity for this aquifer.

| r (ft) | ho - h(ft) |
| --- | --- |
| 50 | 54.9 |
| 150 | 45.5 |
| 250 | 41.1 |
| 500 | 35.2 |
| 1000 | 29.2 |
| 3000 | 19.8 |
| 6000 | 13.9 |
| 10000 | 9.7 |

5. Using your data from the college farm piezometer, calculate hydraulic conductivity (cm/s) of the aquifer.  Is your value for K reasonable for the given geology of the aquifer? (Do not answer this question now, but be ready to answer a similar one for your final exam).