Hydrogeology - Problem Set 1

Due Dates:

Group B, Wednesday, September 19

Group A, Monday, September 24

Unless otherwise stated, report all findings in values of meters and seconds.

1. Following a storm, the flow of a river at the start of pure baseflow discharge was 712 m3/s; after 60 days the flow declined to 523 m3/s.  What would be the flow after 400 days?

2.  (Hypothetically) The city of Harrisonburg decides to look for supplementary water source for the impeding urbanization expected in the region for the next three decades. They will need to withdraw 5 million cubic feet of water per day from the South River near Harriston, with the stipulation that they can never take more than 10% of the total flow of the stream at any time (e.g., 5 million cubic feet of withdraw requires a minimum of 50 million cubic feet to be present). They need a guarantee that this flow rate will be present 90% of the time. Using your knowledge of daily duration curves and the Harriston gaging station, determine how much water (cubic feet per day) can be expected at 90% of the time, and if the 90% rule will be enough for Harrisonburg’s needs given the stated restrictions.

3.  A rectangular weir is placed in a small stream to measure flow.  The horizontal width of the opening is 1.5 ft, and the water rises to a height of 0.22 ft.

- Calculate the discharge of the stream, being very aware of the units that you use for your analysis.

- Approximately, what is the maximum size (intermediate axis) of rip rap (boulder-cobble sized material) that would be stable (non-mobile) under these conditions if the channel has a cross sectional area of 2 m2? (Hint: you will need the Costa Eq. to solve this problem.)

4.  An industrial park with flat-roofed buildings, large parking lots, and little open area has a drainage basin area of 398 acres, located in Rockingham County.  The 5-year rainfall event produced a time of concentration of 32 minutes.

a) What is the maximum rate that overland flow will drain from the industrial park?

b) If the earth material comprising the stream bed is comprised of fine sand, what is the minimum cross sectional area required for stability?

5.  A winding natural stream with weeds has an average depth of 0.86 m and is 7.25 m across. The stream channel drops 0.34 m for each km horizontally. What is the average velocity of the stream?